## Slide 1: 10 Meter Repeaters
Presented at the Arizona State Convention
Williams, AZ July 17, 2009
By Keith Schlottman, KR7RK
Treasurer, 10-10 International Net

## Slide 2: Frequencies
  Coordinated Pairs
  520/620, 540/640, 560/660, 580/680 (normal offset is 100 kHz) – varies by IARU region
  Simplex
  29.600, 29.500
  Linked Systems
  2m or 70 cm  10m
All 10m Repeaters Operate in the Upper Portion of the Band

## Slide 3: Repeater Design
Not Always “Hot”
Owners may turn off
Low Power
Usually 100 watts or less
Omnidirectional Antennas
Normally vertically polarized antennas
Separate TX/RX Antenna
10m duplexers are big and hard to find;
physically separated systems normal

## Slide 4: Repeater Design - 2
Mountaintop / High Sites not critical
Unblocked, low angle of radiation more important
Linked Systems Common
Allows 2 m or 70 cm users to enjoy HF
Geographical Separation
Best to not have nearby 10m repeaters
Often Requires High Level of Technical Skill
Can’t just buy it off the shelf

## Slide 5: What You Need to Operate
HF Multiband Rigs
On some rigs, need to use “split” function
Smaller 10 Meter FM Capable Rigs
Alinco DR-03T
Some “CB-Style” Rigs Have FM Capability
Ranger, Galaxy, Stryker
Older Rigs from Realistic, President, Azden
Yaesu FT-8900R

## Slide 6: What You Need to Operate-2
Handheld 10m Rigs Do Exist But Hard to Find
Midland, Cherokee, Azden, Titan, etc.
May Need to Add a PL Tone Board
Many HF rigs do not have PL as standard
Tune Your Antenna for Higher Frequency
But many 10 meter antennas have a fairly wide bandwidth

## Slide 7: Signal & Propagation Characteristics
Unpredictable
Not reliable for critical communications
Capture Effect
Band openings may result in chaos
Wider Signal Bandwidth than SSB
Can make it difficult to tune precisely, increases QRM; Sounds much different
DX is Possible
Many foreign repeaters

## Slide 8: Web Resources
Worldwide Repeater List
www.hb9hd.ch (a bit out of date)
Detailed Description of a 10m Repeater
www.ipass.net/~teara/2962.html
Ten-Ten International Net, Inc.
www.ten-ten.org
10 Meter FM Yahoo Group
groups.yahoo.com/group/AR29MHz-FM

## Slide 9: Written Resources
ARRL Repeater Directory
Band plans, lingo, repeater listings
ARRL Operating Manual
Chapter on FM and repeaters
AC6V’s FM101x Using FM Repeaters